## Slide 2: Hands on training Non Clinical PKPD data exploration
15 June 2022
Sven Hoefman
Tamara van Steeg

## Slide 3: Concepts

## Slide 4: Population modelling: Illustrative example
Quantification of inter individual variability and residual error
Fictive example : Individual (line connections) PK profiles after single subcutaneous dose
Volume of distribution
Ka
CL
Patients/Animals are different
Assays are subjected to error
Exploration of covariate effects e.g. Different formulation with faster absorption
Difference observation
and individual prediction
measurement error
Outlier evaluation

## Slide 5: PK-PD-Effect integrated modeling
Dose  Concentration  PD response  Clinical effect
  Integrate pharmacokinetic, pharmacodynamic and physiological principles
Sheiner (1992) Learning and confirming in clinical drug development, CPT
Data integration
Across time points
Across doses
Across endpoints
Across studies, populations and species
  Evaluate and quantify differences in patient populations (e.g. disease severity), species …
  Analysis of sparse data is possible: Leverage information from rich (sub)studies
Across drugs

## Slide 6: Population modeling as a tool to integrate and summarize PK-PD-Response knowledge
-PK: clearance (CL), volume of distribution (V) ...
-PD: production (Kin), degradation (Kdeg), drug effect ...
-IIV: Unexplained inter individual variability
-Residual (measurement) error
Explained inter individual variability:
-PK: CL, V increase with body weight
-PD: Kdeg decreases with body weight
-Compound specific effects to be investigated
Population model as tool to answer questions
  Try to capture the most important processes
    Keep it as simple as possible
    But not too simple
  Helps summarize all available knowledge
  Responses are described in a quantitative fashion
  Information from different sources can be integrated
  Allows data driven hypothesis testing
  Model simulations
    predictions can be used to explore untested situations to support decision making
Covariate
model
Structural
model
Statistical
model
Three main components of a population model

## Slide 7: Selection of model type depends on question, data and knowledge of the system
Model types
  Non-compartmental models
    Basic description of observations using linear regression
  Descriptive compartmental models
    A series of interconnected compartments without any physiological interpretation
  Semi-mechanistic compartmental models
    A series of interconnected compartments with some physiological interpretation
  Systems pharmacology - physiologically based PK models
    PBPK: A series of interconnected compartments where each compartment represents a specific organ
Straightforward reporting and interpretation
Purely descriptive -
often limited value in predictions
Drug independent & systems based; High value predictions and extrapolation possible
Time consuming
(months to years)
Align model type choice to
-question
-available data
-system knowledge
Often feasible to develop/update along with drug development
Discuss assumptions and limitations
Predictions possible within boundaries

## Slide 8: Introduction to data exploration app

## Slide 9: Practical information
Link to shiny data exploration application
  Account creation invitation via email address
Live demonstration by Sven Hoefman: use of application
  App developer (Richard Hooijmaijers) available online during course for help
App remains accessible for certain period of time to allow participants to complete / re-visit exercises

## Slide 10: Data exploration shiny app: essentials
App designed for the present course: create explorative graphs for a dataset
  All needed datasets are listed
Getting started
  Select dataset: “sm_rat_pk_iv_sd.csv” (Optional: Click Table source data to get tabular overview)
  Select plotting panel (Default plotting)
    Select following in Layer 1  X value: “TIME”; Y value: “Cplasma”
    Click create plots
      Expand settings as desired  Create plots to re-generate plot
      Re-set settings to starting point via “Clear fields”
  Alternative: create plot via “show presets”
Additional options
  “Create plotly” instead of “create plots”  Interactive version of plot
  Expert plotting: Allows more flexibility and plotting options  but less intuitive for users new to R programming
  Save button to save plots
  Complete refresh can be helpful:

## Slide 11: Explanation of dataset column names
ID: animal number
TIME: time (h)
DOSE_MGKG: dose (mg/kg)
CMPD: compound (SM, mAb)
SPEC: species (Monkey, Rat, Mouse)
BW: body weight (kg)
ROUTE: route of administration (1: IV; 2: PO)
NDOS: number of doses
ADA: Animal anti drug antibody status (0: No; 1: Yes)
C: Concentration (µg/mL), e.g. Cplasma, Cbrain
BQL: Below quantification limit (0: No; 1: Yes)
DV: Dependent variable
BSL: Baseline (for efficacy and Safety biomarker)
Percchange: Percent change from baseline (for efficacy and Safety biomarker)
For the PKPD dataset, two differently structured datasets with same information is provided
  Table “long” versus “wide”
    Long: values of all variables in DV column; TYPE column specifies variable
      TYPE: Cplasma, Cbrain, Efficacy_Biomarker, Safety_Biomarker
    Wide: each variable as a separate column
      Cplasma, Cbrain, Efficacy_Biomarker, Safety_Biomarker, Efficacy_Baseline, Safety_Baseline, Efficacy_Percchange, Safety_Percchange

## Slide 12: Hands on introduction

## Slide 13: Fictive non clinical drug development case – Compound properties
Simplified compound properties + mechanisms of action
  Selection between two lead compounds: small molecule and monoclonal antibody
Drug | SM | mAb
Format | Small molecule | Antibody
Administration | PO | SC
Target Selectivity | 1A receptor 1B receptor | 1A receptor
In vitro Potency (µg/mL) | 1 µg/mL for 1A receptor | 1 µg/mL for 1A receptor
Cross reactivity | Rodent & NHP | NHP, ±10x worse affinity for rodent
MW (g/mol) | 1000 | 150000
1A receptor mainly expressed in brain, associated increased satiety (desired)
1B receptor mainly expressed in liver, associated with liver toxicity, relevance for potential clinical side effects unknown

## Slide 14: Fictive study data availability
Stepwise, simplified overview of drug development path
  Dosage of 3, 10, 30 mg/kg; N=10 per arm; Set of time-points per study (sequential plasma sampling); Assay LLOQ 0.05 µg/mL
  Step 1-4 can be performed using “default plotting”
    For step 4: “expert plotting” option provides more flexibility
 | Drug | Study Type | Dosing | Species | Exploration datasets
Step 1a | SM | PK | IV Single dose | Rat | Data: sm_rat_pk_iv_sd.csv NCA: sm_rat_nca_iv_sd.csv
Step 1b | SM | PK | IV Single dose | Rat, Monkey, Mouse | Data: sm_trans_pk_iv_sd.csv NCA : sm_trans_nca_iv_sd.csv
Step 2 | SM | PK | IV/PO Single dose | Rat | Data: sm_rat_pk_ivpo_sd.csv NCA: sm_rat_nca_ivpo_sd.csv
Step 3 | mAb | PK | IV Single dose | Rat, Monkey | Data: mab_trans_pk_iv_sd.csv NCA: mab_trans_nca_iv_sd.csv
Step 4 | SM + mAb | PKPD | PO/SC Q2D | Rat, Monkey | Data: trans_pkpd_q2d_long.csv; trans_pkpd_q2d_wide.csv

## Slide 15: Purpose / goal(s) during each step
Step 1
  Toolbox practice: raw concentration profiles, NCA analysis results
  Distinguish types of variability: inter- / intra-individual, inter-species
Step 2
  Compare effect of administration routes on PK
Step 3
  Inter-species PK variability for mAbs and its causes
Step 4
  Explore translational PKPD between compounds / doses / species
    Plasma vs brain PK results
    Safety and Efficacy biomarker results
    Recommend safe/efficacious clinical dosing regimen per compound

## Slide 16: Step 1: Assess variability between and within animals
Additional information
  1 week study; 3, 10, 30 mg/kg
Step 1a
  Explore PK profiles and NCA results
    Discuss: variability – between (IIV) and within (measurement error) animals
    Discuss: compare results between dose levels  E.g. Is the PK linear?
Bonus - Step 1b
  Explore NCA results: discuss species differences wrt allometric scaling
 | Drug | Study Type | Dosing | Species | Exploration datasets
Step 1a | SM | PK | IV Single dose | Rat | Data: sm_rat_pk_iv_sd.csv NCA: sm_rat_nca_iv_sd.csv
Step 1b | SM | PK | IV Single dose | Rat, Monkey, Mouse | Data: sm_trans_pk_iv_sd.csv NCA : sm_trans_nca_iv_sd.csv

## Slide 17: Step 2: Compare effect of administration routes on PK
Additional information
  1 week study; 3, 10, 30 mg/kg
Step 2
  Explore and discuss: Compare PK profiles / NCA results between administration routes
Bonus – Step 2
  Discuss: impact of sampling schedule on NCA results
 | Drug | Study Type | Dosing | Species | Exploration datasets
Step 2 | SM | PK | IV/PO Single dose | Rat | Data: sm_rat_pk_ivpo_sd.csv NCA: sm_rat_nca_ivpo_sd.csv

## Slide 18: Step 3: inter-species PK variability for mAbs and its causes
Additional information
  2 week study; 3, 10, 30 mg/kg
Step 3: Explore based on PK profiles / NCA results:
  Discuss: Compare results between doses in monkey
  Discuss: Compare results in terms of species differences between monkey and rat
Bonus – Step 3
  Generate hypotheses regarding differences between individual animals
    Are there predictors of this variability in the dataset?
 | Drug | Study Type | Dosing | Species | Exploration datasets
Step 3 | mAb | PK | IV Single dose | Rat, Monkey | Data: mab_trans_pk_iv_sd.csv NCA: mab_trans_nca_iv_sd.csv

## Slide 19: Step 4: Translational PKPD
Additional information
  2w study; 3/10/30 mg/kg q2d dosing: Plasma PK + terminal brain PK sampling; PD: two biomarkers: efficacy and safety
  2 datasets contain same information but structured differently, depending on plot of interest dataset can be selected
    Long: values of all variables in DV column; TYPE column specifies variable
    Wide: each variable as a separate column
Step 4
  Explore Plasma vs brain PK results between compounds / doses / species
  Explore Safety and Efficacy biomarker results between compounds / doses / species
Bonus – Step 4
  Explore expert plotting option In general tab: multiple panelling, subsetting and transformation options available
    Underlying R code can be explored via:
  Discuss: impact of time point selection
  Discuss: anticipated recommended safe/efficacious clinical dosing regimen per compound
 | Drug | Study Type | Dosing | Species | Exploration datasets
Step 4 | SM + MAB | PKPD | PO/SC Q2D | Rat, Monkey | Data: trans_pkpd_q2d_long.csv; trans_pkpd_q2d_wide.csv